Specification

Ultrasonic Heat meter

UART Protocol

CONTENT

1.	Request Command Format	1

2.	Meter Reading	1

2.1.	Example	1

3.	Revision	4

- Request Command Format

| Fixed | Start | Type | Address | Control | Length | DI0 DI1 | Serial | Check sum | End |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2 bytes | 1 byte | 1 byte | 7 bytes | 1 byte | 1 byte | 2 bytes | 1 byte | 1 byte | 1 byte |

- Meter Reading

  - Example

Request Command: FE FE 68 20 04 00 70 11 01 74 00 01 03 1F 90 00 35 16

Fixed: 0xFE,0xFE

Start: 0x68

Type: 0x20

ADDRESS: 0x04,0x00,0x70,0x11,0x01,0x74,0x00

Control code: 0x01

Length: 0x03

DI0 DI1: 0x1F,0x90

SER: 0x00

Check sum: 0x35

End: 0x16

    - Address Description

If we can see the meter ID on meter stick is 11700004,

| 0x04 | 0x00 | 0x70 | 0x11 | 01 | 74 | 00 |
| --- | --- | --- | --- | --- | --- | --- |
| 11700004 the same as marked on body | This is size code DN15-00 DN20-01 DN25-02 DN32-03 DN40-04 | Fixed code as factory code |

Response:

FE FE 68 20 04 00 70 11 01 74 00 81 2E 1F 90 00 00 00 00 00 05 00 00 00 00 05 00 00 00 00 17 00 00 00 00 35 00 00 00 00 2C 31 25 00 74 26 00 76 68 01 32 34 08 16 05 19 20 00 08 FB 16

Fixed code (2 bytes): 0xFE,0xFE

Frame start character: 0x68

Type of meter: 0x20

Address (seven byte): 0x04,0x00,0x70,0x11,0x01,0x74,0x00 (address of the meter)

Control code: 0x81

Date length: 0x2E

Date identification: 0x1F,0x90

SER: 0x00

Current cooling capacity: 0x00,0x00,0x00,0x00 (mean 0kWH)

Unit: 0x05 (0.01kWH)

Current calories: 0x05,0x01,0x00,0x00		(mean 000001.05kWH)

Unit: 0x05 (0.01kWH)

Power: 0x00,0x00,0x00,0x00		(mean 0kW)

Unit: 0x17 (0.01kW)

Instantaneous flow rate: 0x00,0x00,0x00,0x00(mean 0m3/h)

Unit: 0x35 (0.01m3/h)

Volume: 0x00,0x00,0x00,0x00(mean 0m3)

Unit: 0x2C (0.01m3)

Water supply temperature: 0x31,0x25,0x00 (0025.31℃)

Backwater temperature: 0x74,0x26,0x00 	(0026.74℃)

Working time(hour):0x76,0x68,0x01 (016876h)

Current time (YYYYMMDDHHMMSS): 0x32,0x34,0x08,0x16,0x05,0x19,0x20

(2019.5.16-8:34:32)

State (refer to CJ-T188-2004 stand 8.3.2):ST1,ST2

Check byte: FB

Terminator:0x16

ST1 byte custom description: all custom bites without define.

ST2 byte custom meaning description:

BIT0,1: Battery power alarm,0: normal

BIT1,1: Temperature sensor short circuit alarm,0: normal

BIT2,1: Temperature sensor break circuit alarm,0: normal

BIT3,1: Flow sensor alarm (empty pipe),0: normal

BIT4,1: Power-off status sign,0: normal

BIT5,1: EE fault,0: normal

BIT6,1: temperature of water less than 3 degree, 0: normal

BIT7,1: temperature of water more than 95 degree,0: normal

- Revision

V1.0.1 2015/1/08

+ First

V1.0.2 2020/4/30

+ Added Revision Page

# Text boxes

Bove Intelligent Technology Co., Ltd

Add: Level 5, Building 5, No. 36, Changsheng South Road, Jiaxing, Zhejiang, China, 314000

Tel: +86 573 83525916

Fax: +86 573 83525912

Email: bove@bovetech.com

www.bovetech.com